Pluto ACE
A 65C02 SBC by Johan Groth
# Introduction
Memory map PLUTO
Start	End	Description
$0000	$7EFF	RAM (32K minus 256 bytes)
$7F00	$7F4F	Five unused decoded I/O Blocks (16 bytes each)
$7F50	$7F5F	VIA1 (16 bytes)
$7F60	$7F6F	VIA2 (16 bytes)
$7F70	$7F7F	ACIA (16 bytes)
$7F80	$7FFF	undecoded I/O blocks (128 bytes)
$8000	$FFFF	EEPROM (32K)

Memory map ACIA
RS1	RS0	R/W	Memory Position	Description
0	0	0	$7F70	TxD
0	0	1	$7F70	RxD
0	1	0	$7F71	Programmed Reset
0	1	1	$7F71	Read Status Register
1	0	0	$7F72	Write Command Register
1	0	1	$7F72	Read Command Register
1	1	0	$7F73	Write Control Register
1	1	1	$7F73	Read Control Register

RS-232 pin layout
Signal abbreviation	Meaning	Signal direction at DTE UART	Logic	DB-9 pin number (standard)	R6551 (DIP) pin
GND	Signal ground			5	1
TxD	Transmitted data	Output	Positive	3	10
RxD	Received data	Input	Positive	2	12
RTS	Request to send	Output	Negative	7	8
CTS	Clear to send	Input	Negative	8	9
DTR	Data terminal ready	Output	Negative	4	11
DSR	Data set ready	Input	Negative	6	17
DCD	Data carrier detect	Input	Negative	1	16

# Schematics
# Construction
## PCB
## Mechanical